## Slide 1: Windowing
Jack Henry jbh48 Cian Phillips cp792 Lab Group 54

## Slide 2: What and why?
A method to analyze signals accurately
In order to put in place the correct improvements
Eg mass dampers have to be tuned to the correct frequency
Windowing can be used for any arbitrary signal
We will look at a specific signal made up of the 3 modes of vibration for the building model we used

## Slide 3: Signal
Mode 1:
3.3Hz

## Slide 4: Signal
Mode 2:
9Hz

## Slide 5: Signal
Mode 3:
13.3Hz

## Slide 6: Signal
Superposition

## Slide 7
Signal generated at 1kHz
1 second of a 10 second signal
Signal

## Slide 8: Applying DFT or FFT
Samples measured across a finite period of time
Here is a 0.5s
(or 2% of signal to 7% of signal)

## Slide 9: The Problem with DFT
Creates discontinuities that are treated as part of the original signal in the DFT
This (along with sampling accuracy) causes Spectral Leakage

## Slide 10: Sampled signal FFT: (10s rectangular window)
Should be getting 3 impulses
Effectively a rectangular window over 0.5s, hence spectral leakage
(Code also limiting resolution)

## Slide 11: Increasing time period
Increased to maximum of 10s
Effectively a rectangular window over 10s

## Slide 12: Increasing time period
Increased to maximum of 10s
Effectively a rectangular window over 10s

## Slide 13: Increasing time period
Increased to maximum of 10s
Effectively a rectangular window over 10s

## Slide 14: Increasing time period
Increased to maximum of 10s
Effectively a rectangular window over 10s

## Slide 15: Increasing time period
Increased to maximum of 10s
Effectively a rectangular window over 10s

## Slide 16: Problems
99% and 100% relative window shown on left
Even with 99% or 100% of signal time lots of spectral leakage
Sensitive to number and placement of discontinuities

## Slide 17: Solution: Different Windows
Apply a window that starts and ends at 0 to eliminate discontinuities
(on small time period for clarity)
Notes: Cian

## Slide 18: Solution: Different Windows
Apply a window that starts and ends at 0 to eliminate discontinuities

## Slide 19: Solution: Different Windows
Apply a window that starts and ends at 0 to eliminate discontinuities

## Slide 20: Solution: Different Windows
Across entire 10 seconds:

## Slide 21: Solution: Different Windows
Across entire 10 seconds:

## Slide 22: Solution: Different Windows
Across entire 10 seconds:

## Slide 23: Different Window Spectra
Triangle window spectrum, across entire 10 seconds

## Slide 24: Different Window Spectra
Zoomed in we can see more detail

## Slide 25: What’s actually going on?

## Slide 26: Different windows and their spectra
(Aka
Bartlett)
Hamming doesn’t start and end at 0
Kaiser has a ‘narrowing’ parameter
Some of many windows

## Slide 27: What’s good?
Characteristics:
  Main lobe width
  Side lobe max
  Side lobe roll-off
Two or more signals very near to each other = a very narrow main lobe
Amplitude accuracy of a single frequency component more important than location = wide main lobe
Flat signal spectrum = Uniform/rectangular window (no window)
Hann window is satisfactory in 95% of cases - good frequency resolution and reduced spectral leakage.
Notes: Jack

## Slide 28: Applied to our signal
Generally, there is a compromise between main lobe width and spectral leakage

## Slide 29: Applied to our signal
Generally, there is a compromise between main lobe width and spectral leakage

## Slide 30: Applied to the building
Hanning best for compromise
Rectangular best for accuracy if need to fine tune mass dampers

## Slide 31: Applied to the building
Hanning best for compromise
Much lower spectral leakage for high frequencies
Changes when noise is introduced….

## Slide 32: Thank you Any Questions?
https://en.wikipedia.org/wiki/Window_function
https://www.sjsu.edu/people/burford.furman/docs/me120/FFT_tutorial_NI.pdf

## Slide 33
import numpy as np
from numpy.fft import fft, fftfreq
import matplotlib.pyplot as plt
signaltime = 10 # time that signals run for
sr = 1000 # sample rate (per second)
sp = 1/sr # sample interval
sn = signaltime *sr # number of samples
t = np.linspace(0,signaltime, sn) # time array
def signal(f1,f2,f3, noise=False):
signals = ([f1,1],[f2,1], [f3,1]) # signals generated (based on mode frequencies)
sig = np.zeros(len(t)) # 0 array for signals
if noise==False:
for i in signals: # effectively sampling the signals at desired sample rate and superposing over each other
sig += i[1] * np.sin(2 * np.pi * i[0] * t) # + np.random.rand(t.size))
if noise==True:
for i in signals: # with noise
sig += i[1] * np.sin(2 * np.pi * i[0] * t + np.random.rand(t.size))
return sig
f1 = 3.3
f2 = 9
f3 = 13.3
signal = signal(f1,f2,f3, noise=True)
uw = (1/100)*100 #percentage of total time for window
lw = (1/100)*0
windowupper = int(uw*signaltime*sr) # upper window limit (in time)
windowlower = int(lw*signaltime*sr) # lower window limit (in time)
windowwidth = windowupper - windowlower # window width (in time), and also number of samples within window
sampledsignal = signal[windowlower:windowupper] # sampled signal only in windowed time space
wf1 = np.hamming(windowwidth) # creating hamming window function
ws1 = sampledsignal*wf1 # applying hamming window to reduced sampled signal
wf2 = np.bartlett(windowwidth) # creating bartlett window
ws2 = sampledsignal * wf2 # applying bartlett window to reduced sampled signal
wf3 = np.blackman(windowwidth)
ws3 = sampledsignal *wf3 # creating and applying blackman window to reduced sampled signal
wf4 = np.hanning(windowwidth)
ws4 = sampledsignal *wf4
wf5 = np.kaiser(windowwidth,14)
ws5 = sampledsignal *wf5
repeats = -(sn // -windowwidth) +1
repeatedsampledsignal = np.tile(sampledsignal,repeats)[windowwidth-windowlower%windowwidth:(windowwidth-windowlower%windowwidth)+sn]
x = fftfreq(sn, sp)[:sn//2]
y = fft(signal)[:sn//2]
xf = fftfreq(windowwidth, sp)[:windowwidth//2] # frequency array
yf = fft(sampledsignal)[:windowwidth//2] # FFT of sampled signal
yfw1 = fft(ws1)[:windowwidth//2] # FFT of sampled signal with hamming window
yfw2 = fft(ws2)[:windowwidth//2] # FFT of sampled signal with bartlett window
yfw3 = fft(ws3)[:windowwidth//2] # FFT of sampled signal with blackman window
yfw4 = fft(ws4)[:windowwidth//2] # FFT of sampled signal with hanning window
yfw5 = fft(ws5)[:windowwidth//2] # FFT of sampled signal with kaiser window
yw1 = fft(wf1)[:windowwidth//2] # FFTs of purely the window
yw2 = fft(wf2)[:windowwidth//2]
yw3 = fft(wf3)[:windowwidth//2]
yw4 = fft(wf4)[:windowwidth//2]
yw5 = fft(wf5)[:windowwidth//2]

## Slide 34: Noise

## Slide 35: Windows (python)